## Slide 2: Plan for this week
Tuesday:
The Raster Data Model
Thursday:
Map Algebra
  Local operations

## Slide 3: What is spatial analysis
Goes beyond maps and mapping
  Visualization is at the most basic end
Link data to location
  Identifying data based on a location
  Explore the relationship between data (variables)
  Extend that into the realms of explanation and prediction
Data has to be linked by ID/OID/FID, space-time, and include some attribute
Not necessary to have the same location/time
  Surface flow through a watershed
  Precipitation amounts through time
  Spending locations across a city

## Slide 4: How can Spatial Analysis Help
Deriving Spatial relationships (finding the links)
  Sometimes called “Teleconnections” in literature
    ENSO cycles
  Reveal spatial relationships that might otherwise be “invisible”
  Make explicit what is implicit
    Spatial connectivity
      Groundwater flow from one basin to another
    DEM analysis
      Watershed, terrain shadow, viewsheds
    Spatial correlation and auto-correlation
Continuum of sophistication
  Mapping -> Queries -> Complex statistical methods (interpolation, PCA)
Notes: La Niña is the positive or cold phase of the Pacific. When this occurs, sea surface temperatures, from near the South American coast westward into the equatorial Pacific, will drop below normal, while abnormally high air pressure keeps the atmosphere stable. Southern California will typically see below-normal rainfall during La Niña phases. In fact, a large chunk of our current four-year drought played out during a La Niña event. Meanwhile, the western Pacific experiences abnormally low air pressure and stormy weather.
The negative or warm phase of the Pacific is called El Niño. During El Niño, the equatorial sea surface temperatures across the eastern Pacific, particularly off the South American coast, climb well above average. Abnormally low pressure dominates the eastern Pacific while abnormally high pressure is in place across Indonesia. For Southern California, strong El Niño phases generally produce above normal rainfall.
http://ktla.com/2015/10/14/el-nino-2015-defining-el-nino/

## Slide 5: What Questions/Phenomenon
Effective analysis are “tailor made” for certain problems
  Cellphone tower siting
Methods were originally made for applications
Retooled for generalized application
Essential to identify and understand a domain
  Know the domain
  Know what you are looking for
  Apply findings to analysis
I’m biased towards the physical systems

## Slide 6: Raster or Vector?
 | Raster | Vector
Definitions | Gridded data, spatially associated with itself Larger files Best represents a continuum Simple data structure | Geometrically and mathematically associated Points, lines, polygons Single & Multipart
Tradeoffs | Overlay analyses are easily and efficient HPC friendly High variability more efficiently represented How screens work | More compact data structure Smaller files More “accurate” More amenable to network analysis Visually appealing
Raster's tell us where things are everywhere and vector tells us where everything is |  | 

## Slide 7: The Raster Data Model

## Slide 9: Raster Datasets
A matrix of numbers
Cell value statistics
Storage
  2D array vs run-length encoding
  Very large raster's
  Multiple resolutions
  Computer Formats
What makes a raster different from and image?
  Spatial reference
  Explicit cell size and spatial extent

## Slide 11: Storing Cell Values
2D array
  Stored cell by cell as a 2D array
Run Length Encoding
  Stored as a list of (value) (occurrence)
Does run length encoding guarantee compression?

## Slide 13
Disk based storage
  Does not have to all be in memory ay once
  Parallelization analysis

## Slide 18: Why Tile?

## Slide 19: Tiling

## Slide 20: Why Tile?
Notes: Build pyramids? Yes.

## Slide 21: Raster Formats
Tiff
  Geotiff
  .tfw
JPG
  Jpg2000
  .jpw
netCDF*
ASCII

## Slide 24: Mixed Pixels

## Slide 25: Spatial Resolution and Mixels

## Slide 28: Remote Sensing Concepts
Resolution
  Radiometric
  Spectral
  Spatial
  Temporal
Discrete vs. Continuous measurements
Electromagnetic Radiation and Spectral Signatures

## Slide 29: Radiometric Resolution
Number of brightness levels that can be detected by the sensor
Also known as radiometric sensitivity, quantization, or simply the number of bits per pixel

## Slide 30: Spectral Resolution
Number of bands on the sensor
Bandwidth
Band location on the spectrum

## Slide 31: Spatial Resolution

## Slide 32: Resolution Concepts: Temporal

## Slide 33: Swath Comparison

## Slide 34: Time of Day
Most sensors acquire their images in mid to late morning (i.e., between around 9:30 and 11:00 a.m.)
A few acquire images in the early afternoon (e.g., 2:00 to 2:30)
Some sensors are able to acquire images at night

## Slide 35: Multispectral Layer Stack