## Slide 1
Notes: http://iceland.carto.com/tables/iceland/embed_map?title=true&description=true&search=false&shareable=false&cartodb_logo=true&sql=

## Slide 4: Robustness and Resistance
Robustness and resistance are two aspects of insensitivity to assumptions about the nature of a set of data.
Robust methods are not sensitive to particular assumptions about the overall nature of the data. A robust method is not necessarily optimal in any particular circumstance, but performs reasonably well in most circumstances.
Resistant methods are not unduly influenced by a small number of outliers, or error data values.

## Slide 5: ArcGIS Interpolation methods
Deterministic
  IDW (Inverse Distance Weighted)
  Natural neighbor
  Trend
  Spline
  Spline with Barriers
Geostatistical
  Kriging
Methodological
  Topo to Raster

## Slide 6: Spatial Interpolation
The official ESRI definition of kriging is “an interpolation technique in which the surrounding measured values are weighted to derive a predicted value for an unmeasured location’.
This basically means that measured values help to interpolate or define values for those that are unknown.
Kriging is different from other spatial interpolation techniques because it is able to assess the quality of predicted values and thus, not all points need to be measured and/or known (Chang, 2012).

## Slide 7: Interpolation and the First Law of Geography
Tobler’s First Law
“Everything is related to everything else, but near things are more closely related than distant things”
Interpolation: Determining unknown values from known measurements

## Slide 9: Global Interpolation Methods
Global interpolation
  use all samples to estimate the value at an unsampled location
Data fitting using all the samples
  Z=f(x,y)
Trend surface models (polynomial equations)
  A first-order trend surface simply fit a 3D plane to all the sample points.
    Z = b0 + b1x + b2y
  Higher order polynomial functions could fit more complex surfaces to sample points
    Z = b0 + b1x + b2y + b3xy + b4x2+ b5y2
  Other forms of the functions
    Whether the surface passes the sample points

## Slide 13: Local Interpolation Methods
Every thing is related to everything else. Near things are more related than distant things (First law of geography)
Local interpolation
  use nearby samples to estimate at an unsampled location
  Near things are more similar than distant things
How can the first law of geography be used in spatial interpolation
  Using nearby samples
  How near is “nearby”?
  How to combine nearby values?
Simple local interpolation methods
  Nearest neighbor results into Thiessen’s polygons
  Inverse distance weighted (IDW)

## Slide 14
Notes: https://www.youtube.com/watch?v=5oScAPFAVi0

## Slide 17
Notes: https://www.youtube.com/watch?v=5oScAPFAVi0

## Slide 18: How to Quantify the Similarity (or difference) in Space
Two locations close to each other are more likely to have similar values than two location that are far apart
  spatial autocorrelation
How similar is a variable to itself in space?
  Different variables have different (spatial) similarities
  Same variable may have different similarity in different direction (anisotropy)
How to quantify (or model) the spatial similarity (or difference)?

## Slide 19: Statistical interpolation
Unlike it’s deterministic counterparts, Kriging considers the spatial relationships of the measured points.
  This means that we can not only say what a value is at a given point, but also how certain we are of that prediction.
Kriging assumes that the distance or direction between sample points reflects a spatial correlation that can be used to explain variation in the surface. The Kriging tool fits a mathematical function to a specified number of points, or all points within a specified radius, to determine the output value for each location.

## Slide 30
But what is a Correlogram?
How do I get a Semi-Variogram?
Why?

## Slide 31
Notes: https://www.youtube.com/watch?v=SJLDlasDLEU